As a part of your end year networking project, you are required to design and implement Vic Modern Hotel network. The hotel has three floors, in the first floor there three departments (Reception, Store, and Logistics), in second floor there are three departments (Finance, HR , and Sales Marketing), while the third floor hosts the IT and Admin. Therefore, the following are part of the considerations during the design and implementation.

There should be three routers connecting each floor (all placed in the server room in IT department).
- All routers should be connected to each other using serial DCE cable.
- The network between the routers should be
- 10.10.10.0/30
- 10.10.10.4/30
- 10.10.10.8/30
- Each floor is expected to have one switch(placed in the respective floor)
- Each floor is expected to have WIFI networks connected to laptops and phones.
- Each department is expected to have a printer.
- Each department is expected to be in different VLAN with the following details.

1st Floor

- Reception	- VLAN 80	Network of 192.168.8.0/24
- Store	- VLAN 70	Network of 192.168.7.0/24
- Logistics	- VLAN 60	Network of 192.168.6.0/24

2nd Floor

- Finance	- VLAN 50	Network of 192.168.5.0/24
- HR	- VLAN 40	Network of 192.168.4.0/24
- Sales	- VLAN 30	Network of 192.168.3.0/24

3rd Floor

- Admin	- VLAN 20	Network of 192.168.2.0/24
- IT	- VALN 10	Network of 192.168.1.0/24

- Use OSPF as the routing protocol to advertise routers.
- All devices in the network are expected to obtain IP address dynamically with their respective router configured as the DHCP server.
- All the devices in the network are expected to communicate with each other.
- Configure SSH in all the routers for remote login.
- In IT department, add PC called Test-PC to port fa0/1 and use it to test remote login.
- Configure port security to IT-dept switch to allow only Test-PC to access port fa0/1 (Use sticky method to obtain mac-address with violation mode of shutdown)

Routers Cisco 2911

We can’t connect serial DCE cables any default interfaces in the router. So we have to add serial interfaces to routers manually.

1. Power off the router using power button located in behind the router.
2. Choose HWIC-2T from modules and place that in an empty slot of the router.
3. Power on the router.

     Connections :

F1-Router se0/0/1 --------- F2-Router se0/0/0
F1-Router se0/0/0 --------- F3-Router se0/0/0
F2-Router se0/0/1 --------- F3-Router se0/0/1

F1-Router (10.10.10.1) ------ 10.10.10.0/30 ------ F2-Router (10.10.10.2)
F1-Router (10.10.10.5) ------ 10.10.10.4/30 ------ F3-Router (10.10.10.6)
F2-Router (10.10.10.9) ------ 10.10.10.8/30 ------ F3-Router (10.10.10.10)

We have connected routers using serial DCE cables. To forward traffic through those interfaces we have to enable clock rate of serial DCE interfaces. We can identify the DCE interfaces using clock symbol in the interface.

F1-Router

Interface	Connected Device
Se0/0/0 DCE end(Enable Clock Rate)	F3-Router Se0/0/0
Se0/0/1 DCE end(Enable Clock Rate)	F2-Router Se0/0/0
Gig0/0	F1-Switch Fa0/1

Configuration :

Hostname, password and banner are configured.

password : sande

Enable interfaces :

Router> enable
Router# conf t

Router(config)# interface se0/0/0
Router(config-if)# no shutdown
Router(config-if)# clock rate 64000
Router(config-if)# exit

Router(config)# interface se0/0/1
Router(config-if)# no shutdown
Router(config-if)# clock rate 64000
Router(config-if)# exit

Router(config)# interface g0/0
Router(config-if)# no shutdown
Router(config-if)# exit

Configuring IP address for router interfaces :

F1-Router(config)#interface se0/0/1
F1-Router(config-if)#ip address 10.10.10.1 255.255.255.252

F1-Router(config)#interface se0/0/0
F1-Router(config-if)#ip address 10.10.10.5 255.255.255.252

Configuring Inter VLAN routing :

    We have to divide g0/0 interface to sub interfaces.

F1-Router(config)#interface g0/0.80
F1-Router(config-subif)#encapsulation dot1Q 80
F1-Router(config-subif)#ip address 192.168.8.1 255.255.255.0

F1-Router(config)#interface g0/0.70
F1-Router(config-subif)#encapsulation dot1Q 70
F1-Router(config-subif)#ip address 192.168.7.1 255.255.255.0

F1-Router(config)#interface g0/0.60
F1-Router(config-subif)#encapsulation dot1Q 60
F1-Router(config-subif)#ip address 192.168.6.1 255.255.255.0

Configuring DHCP :

F1-Router(config)#service dhcp

F1-Router(config)#ip dhcp pool RECEPTION
F1-Router(dhcp-config)#network 192.168.8.0 255.255.255.0
F1-Router(dhcp-config)#default-router 192.168.8.1
F1-Router(dhcp-config)#dns-server 192.168.8.1

F1-Router(config)#ip dhcp pool STORE
F1-Router(dhcp-config)#network 192.168.7.0 255.255.255.0
F1-Router(dhcp-config)#default-router 192.168.7.1
F1-Router(dhcp-config)#dns-server 192.168.7.1

F1-Router(config)#ip dhcp pool LOGISTICS
F1-Router(dhcp-config)#network 192.168.6.0 255.255.255.0
F1-Router(dhcp-config)#default-router 192.168.6.1
F1-Router(dhcp-config)#dns-server 192.168.6.1

Configuring Routing Protocol (OSPF protocol) :

F1-Router(config)#router ospf 10

F1-Router(config-router)#network 10.10.10.0 255.255.255.252 area 0
F1-Router(config-router)#network 10.10.10.4 255.255.255.252 area 0

F1-Router(config-router)#network 192.168.8.0 255.255.255.0 area 0
F1-Router(config-router)#network 192.168.7.0 255.255.255.0 area 0
F1-Router(config-router)#network 192.168.6.0 255.255.255.0 area 0

Configuring SSH :

F1-Router(config)#ip domain-name sande
F1-Router(config)#username sande password sande
F1-Router(config)#crypto key generate rsa
How many bits in the modulus [512]: 1024
F1-Router(config)#line vty 0 15
F1-Router(config-line)#login local
F1-Router(config-line)#transport input ssh

F2-Router

Interface	Connected Device
Se0/0/0	F1-Router Se0/0/1
Se0/0/1 DCE end(Enable Clock Rate)	F3-Router Se0/0/1
Gig0/0	F2-Switch Fa0/1

Configuration :

Hostname, password and banner are configured.

password : sande

Enable interfaces :

F2-Router(config)# interface se0/0/0
F2-Router(config-if)# no shutdown
F2-Router(config-if)# exit

F2-Router(config)# interface se0/0/1
F2-Router(config-if)# no shutdown
F2-Router(config-if)# clock rate 64000
F2-Router(config-if)# exit

F2-Router(config)#interface g0/0
F2-Router(config-if)#no shutdown
F2-Router(config-if)#exit

Configuring IP address for router interfaces :

F2-Router(config)#interface se0/0/0
F2-Router(config-if)#ip address 10.10.10.2 255.255.255.252

F2-Router(config)#interface se0/0/1
F2-Router(config-if)#ip address 10.10.10.9 255.255.255.252

Configuring Inter VLAN routing :

    We have to divide g0/0 interface to sub interfaces.

F2-Router(config)#interface g0/0.50
F2-Router(config-subif)#encapsulation dot1Q 50
F2-Router(config-subif)#ip address 192.168.5.1 255.255.255.0

F2-Router(config)#interface g0/0.40
F2-Router(config-subif)#encapsulation dot1Q 40
F2-Router(config-subif)#ip address 192.168.4.1 255.255.255.0

F2-Router(config)#interface g0/0.30
F2-Router(config-subif)#encapsulation dot1Q 30
F2-Router(config-subif)#ip address 192.168.3.1 255.255.255.0

Configuring DHCP :

F2-Router(config)#service dhcp

F2-Router(config)#ip dhcp pool FINANCE
F2-Router(dhcp-config)# network 192.168.5.0 255.255.255.0
F2-Router(dhcp-config)#default-router 192.168.5.1
F2-Router(dhcp-config)#dns-server 192.168.5.1

F2-Router(config)#ip dhcp pool HR
F2-Router(dhcp-config)#network 192.168.4.0 255.255.255.0
F2-Router(dhcp-config)#default-router 192.168.4.1
F2-Router(dhcp-config)#dns-server 192.168.4.1

F2-Router(config)#ip dhcp pool SALES
F2-Router(dhcp-config)#network 192.168.3.0 255.255.255.0
F2-Router(dhcp-config)#default-router 192.168.3.1
F2-Router(dhcp-config)#dns-server 192.168.3.1

Configuring Routing Protocol (OSPF protocol) :

F2-Router(config)#router ospf 10

F2-Router(config-router)#network 10.10.10.0 255.255.255.252 area 0
F2-Router(config-router)#network 10.10.10.8 255.255.255.252 area 0

F2-Router(config-router)#network 192.168.5.0 255.255.255.0 area 0
F2-Router(config-router)#network 192.168.4.0 255.255.255.0 area 0
F2-Router(config-router)#network 192.168.3.0 255.255.255.0 area 0

Configuring SSH :

F2-Router(config)#ip domain-name sande
F2-Router(config)#username sane password sande
F2-Router(config)#crypto key generate rsa
How many bits in the modulus [512]: 1024
F2-Router(config)#line vty 0 15
F2-Router(config-line)#login local
F2-Router(config-line)#transport input ssh

F3-Router

Interface	Connected Device
Se0/0/0	F1-Router Se0/0/0
Se0/0/1	F2-Router Se0/0/1
Gig0/0	F3-Switch Fa0/2

Configuration :

Hostname, password and banner are configured.

password : sande

Enable interfaces :

F3-Router(config)# interface se0/0/0
F3-Router(config-if)# no shutdown
F3-Router(config-if)# exit

F3-Router(config)# interface se0/0/1
F3-Router(config-if)# no shutdown
F3-Router(config-if)# exit

F3-Router(config)# interface g0/0
F3-Router(config-if)# no shutdown
F3-Router(config-if)# exit

Configuring IP address for router interfaces :

F3-Router(config)#interface se0/0/0
F3-Router(config-if)#ip address 10.10.10.6 255.255.255.252

F3-Router(config)#interface se0/0/1
F3-Router(config-if)#ip address 10.10.10.10 255.255.255.252

Configuring Inter VLAN routing :

    We have to divide g0/0 interface to sub interfaces.

F3-Router(config)#interface g0/0.20
F3-Router(config-subif)#encapsulation dot1Q 20
F3-Router(config-subif)#ip address 192.168.2.1 255.255.255.0

F3-Router(config)#interface g0/0.10
F3-Router(config-subif)#encapsulation dot1Q 10
F3-Router(config-subif)#ip address 192.168.1.1 255.255.255.0

Configuring DHCP :

F3-Router(config)#service dhcp

F3-Router(config)#ip dhcp pool ADMIN
F3-Router(dhcp-config)#network 192.168.2.0 255.255.255.0
F3-Router(dhcp-config)#default-router 192.168.2.1
F3-Router(dhcp-config)#dns-server 192.168.2.1

F3-Router(config)#ip dhcp pool IT
F3-Router(dhcp-config)#network 192.168.1.0 255.255.255.0
F3-Router(dhcp-config)#default-router 192.168.1.1
F3-Router(dhcp-config)#dns-server 192.168.1.1

Configuring Routing Protocol (OSPF protocol) :

F3-Router(config)#router ospf 10

F3-Router(config-router)#network 10.10.10.4 255.255.255.252 area 0
F3-Router(config-router)#network 10.10.10.8 255.255.255.252 area 0

F3-Router(config-router)#network 192.168.2.0 255.255.255.0 area 0
F3-Router(config-router)#network 192.168.1.0 255.255.255.0 area 0

Configuring SSH :

F3-Router(config)#ip domain-name sande
F3-Router(config)#username sande password sande
F3-Router(config)#crypto key generate rsa
How many bits in the modulus [512]: 1024
F3-Router(config)#line vty 0 15
F3-Router(config-line)#login local
F3-Router(config-line)#transport input ssh

Switches Cisco 2960

F1-Switch

Interface	Connected Device
Fa0/1	F1-Router Gig0/0
Fa0/2	F1-Access-Point
Fa0/3	PC0
Fa0/4	Printer0
Fa0/5	PC1
Fa0/6	Printer1
Fa0/7	PC2
Fa0/8	Printer2

VLANs :

Reception	- VLAN 80	Network of 192.168.8.0/24	fa0/3, fa0/4
Store	- VLAN 70	Network of 192.168.7.0/24	fa0/5, fa0/6
Logistics	- VLAN 60	Network of 192.168.6.0/24	fa0/7, fa0/8

Configurations:

Host name, password and banner are configured.

password : sande

Creating VLANS

For Reception :

F1-SWITCH(config)# interface range fa0/3-4
F1-SWITCH(config-if-range)# switchport mode access
F1-SWITCH(config-if-range)# switchport access vlan 80

For Store :

F1-SWITCH(config)# interface range fa0/5-6
F1-SWITCH(config-if-range)# switchport mode access
F1-SWITCH(config-if-range)# switchport access vlan 70

For Logistics :

F1-SWITCH(config)# interface range fa0/7-8
F1-SWITCH(config-if-range)# switchport mode access
F1-SWITCH(config-if-range)# switchport access vlan 60

Configure trunk ports :

F1-SWITCH(config)#interface fa0/1
F1-SWITCH(config-if)#switchport mode trunk

For access point :

we have to add access point to the department VLAN. So I will add this 1st floor	access point to Reception VLAN 80.

F1-SWITCH(config)#interface fa0/2
F1-SWITCH(config-if)#switchport mode access
F1-SWITCH(config-if)#switchport access vlan 80

F2-Switch

Interface	Connected Device
Fa0/1	F2-Router Gig0/0
Fa0/2	F2-Access-Point
Fa0/3	PC3
Fa0/4	Printer5
Fa0/5	PC4
Fa0/6	Printer6
Fa0/7	PC5
Fa0/8	Printer7

VLANs :

Finance	- VLAN 50	Network of 192.168.5.0/24	fa0/3, fa0/4
HR	- VLAN 40	Network of 192.168.4.0/24	fa0/5, fa0/6
Sales	- VLAN 30	Network of 192.168.3.0/24	fa0/7, fa0/8

Configurations:

Host name, password and banner are configured.

password : sande

Creating VLANS

For Finance :

F2-SWITCH(config)#interface range fa0/3-4
F2-SWITCH(config-if-range)#switchport mode access
F2-SWITCH(config-if-range)#switchport access vlan 50

For HR :

F2-SWITCH(config)#interface range fa0/5-6
F2-SWITCH(config-if-range)#switchport mode access
F2-SWITCH(config-if-range)#switchport access vlan 40

For Sales :

F2-SWITCH(config)#interface range fa0/7-8
F2-SWITCH(config-if-range)#switchport mode access
F2-SWITCH(config-if-range)#switchport access vlan 30

Configuring trunk ports :

F2-SWITCH(config)#interface fa0/1
F2-SWITCH(config-if)#switchport mode trunk

F3-Switch

Interface	Connected Device
Fa0/2	F3-Router Gig0/0
Fa0/3	F3-Access-Point
Fa0/1	Test-PC
Fa0/4	Printer4
Fa0/5	PC6
Fa0/6	Printer3

VLANs :

Admin	- VLAN 20	Network of 192.168.2.0/24	fa0/5, fa0/6
IT	- VALN 10	Network of 192.168.1.0/24	fa0/1, fa0/4

Configurations:

Host name, password and banner are configured.

password : sande

Creating VLANS

For Admin :

F3-SWITCH(config)#interface range fa0/5-6
F3-SWITCH(config-if-range)#switchport mode access
F3-SWITCH(config-if-range)#switchport access vlan 20

For IT :

F3-SWITCH(config)#interface f0/1
F3-SWITCH(config-if)#switchport mode access
F3-SWITCH(config-if)#switchport access vlan 10
F3-SWITCH(config-if)#exit
F3-SWITCH(config)#interface fa0/4
F3-SWITCH(config-if)#switchport mode access
F3-SWITCH(config-if)#switchport access vlan 10

Configuring trunk ports :

F2-SWITCH(config)#interface fa0/2
F2-SWITCH(config-if)#switchport mode trunk

configure fa0/1 port security :

F3-SWITCH(config)#interface fa0/1
F3-SWITCH(config-if)#switchport port-security
F3-SWITCH(config-if)#switchport port-security maximum 1
F3-SWITCH(config-if)#switchport port-security mac-address sticky
F3-SWITCH(config-if)#switchport port-security violation shutdown

F1-Access-Point

SSID	: Floor-01-WIFI
password	: floor1@123

F2-Access-Point

SSID	: Floor-02-WIFI
password	: floor2@123

F3-Access-Point

SSID	: Floor-03-WIFI
password	: floor3@123