Design a network in CISCO packet tracer to connect ACCOUNTS and DELIVERY departments through the following:
1. Each department should contain at least 2PCs.
2. Appropriate number of switches and routers should be used in the network
3. Using the given network address 192.168.40.0, all interfaces should be configured with appropriate IP addresses, subnet mask and gateways.
4. All devices in the network should be connected using appropriate cables.
5. Test the connectivity between ACCOUNT and DELIVERY departments. PCs in DELIVERY department should be able to ping PCs in ACCOUNTS department.

Network Address	= 192.168.40.0
No of subnets	= 2

This is a class c address. So subnet mask is /24 or

11111111.11111111.11111111.00000000
255.255.255.0

2^n = no of subnets => 2^n = 2
        => n = 1

so we have to take one bit to create 2 subnets.

11111111.11111111.11111111.10000000
255.255.255.128

subnet mask = 255.255.255.128

1st subnet 192.168.40.0/25

subnet mask	= 255.255.255.128
Network ID	= 192.168.40.0
Valid range for hosts	= 192.168.40.1 – 192.168.40.126
Broadcast ID	= 192.168.40.127

2nd subnet 192.168.40.128/25

subnet mask	= 255.255.255.128
Network ID	= 192.168.40.128
Valid range for hosts	= 192.168.40.129 – 192.168.40.254
Broadcast ID	= 192.168.40.255